## Slide 1: Resource Allocation in Wireless Cellular Networks
M. Rasti
Amirkabir University of Technology

## Slide 2: Course Syllabus
I- Basics of Wireless Networks
  1- Introduction of Wireless Networks and Radio Resources
  2- Categories of Wireless Networks and Taxonomy of Hot Topics Research Areas on Resource Allocation in Wireless Networks
II- Techniques for Modeling and Analysis of Radio Resource Allocation in Wireless Networks
  3- Convex Optimization
  4- Game Theory
III- Physical Layer Resource Allocation in Wireless Networks
  5- General System Model and Preliminary Concepts
  6- Power Control in Wireless Cellular Networks
  7- Joint Power and Admission Control in Cellular Wireless Networks
  8- Cell Association in Cellular Networks
  9- Application of Game Theory in Physical Layer Resource Allocation in Wireless Networks
  10- Joint Power and Admission Control in Cognitive Radio Network

## Slide 3: Power Control in Wireless Cellular Networks Lecture 5 Outline
Performance Measures
Why Power Control?
Closed-Loop and Open-Loop Power Control
Different Power Control Optimization Problems
Distributed Power Control Algorithms
Some Open Problems

## Slide 4: Performance Measures
Performance measures
  Throughput for a user:
  System throughput:
  Total transmit power:
  Outage probability:
  where ,

## Slide 5: Power Control in Wireless Cellular Networks Lecture 5 Outline
Performance Measures
Why Power Control?
Closed-Loop and Open-Loop Power Control
Different Power Control Optimization Problems
Distributed Power Control Algorithms
Some Open Problems

## Slide 6: Why Power Control? Need for Power Control
Power control is needed to resolve near-far problem
Objective of power control is to adjust the transmit power on the downlink and/or uplink in order to satisfy a given objective function
  Minimizing total transmit power
  Maximizing system throughput
  Minimizing outage probability
  Fairness

## Slide 7: Uplink and Downlink Power Control
Power control is needed at both uplink and downlink
Most of the treatment is devoted to uplink transmission from mobile station (MS) to base station (BS), although extensions to downlink transmission from a BS to MSs are sometimes discussed as well
We focus on uplink power control

## Slide 8: SIR at Downlink and Uplink
SIR at uplink
  where is the transmit power set by user and is the path-gain from user to the base station
SIR at downlink ….
  where is the transmit power set by the base-sation for user , and is the path-gain from the base station to user

## Slide 9: Why focusing on uplink power control?
In many formulations uplink problems are more difficult to solve, although there are exceptions like joint power control and beamforming
Uplink power control is also often more important in systems engineering of cellular networks
    BS power consumption is of less importance in comparison to MS power consumption.
    the downlink intra-cell interference is much smaller in comparison to uplink intra-cell interference, because maintaining orthogonality of resource allocation (e.g., code allocation in CDMA, tone allocation in OFDM) to MSs within a cell on the downlink is easily accomplished by the BS

## Slide 10: Power Control in Wireless Cellular Networks Lecture 5 Outline
Performance Measures
Why Power Control?
Closed-Loop and Open-Loop Power Control
Different Power Control Optimization Problems
Distributed Power Control Algorithms
Some Open Problems

## Slide 11: Existing Approaches for Power Control
Cooperative
Non-cooperative
Distributed
Centralized
Power Control
Game-theoretic

## Slide 12: Conventional Centralized Uplink Power Control Schemes in Existing Standards
Open Loop
  Base station transmits at a known power level (a beacon) which mobile measures to estimate the path loss
  Assumes path loss in both directions is the same
  Not very accurate when uplink and downlink are separated in frequency
Closed-Loop
  SIR measured at the receiver and compared to the target-SIR value
  Receiver sends a power control command to transmitter to reduce or increase the power level - requires a bidirectional link
  CDMA2000: 800 commands/sec
  3GPP: 1500 commands/sec

## Slide 13: Uplink Open Loop Power Control
Key rule is that mobile transmits in inverse proportion to power level it receives from BS’s beacon
  If the received power is high, the mobile user reduces its transmit power
  If received power is low, mobile user increases its transmit power
In open loop power control the base station is not involved.

## Slide 14: Flaw in Uplink Open Loop Power Control
Major flaw with this criteria is that uplink propagation statistics are based on downlink propagation statistics
  But since the two links are not correlated a significant error may result from this procedure
These errors will be corrected once the closed loop power control mechanism becomes active
  The closed loop power control provides correction to the open loop power control.

## Slide 15: Close-Loop Power Control Properties
In closed-loop power control, based on power control bit received from the base station, mobile either increases or decreases transmit power
  A zero indicates to the mobile that its should increase its mean output power level.
  A one indicates to mobile to decrease its mean output power level.
Each power bit produces a 1db change in the power

## Slide 16: PCGs
IN CDMA2000, a power control bit 0/1 is transmitted every 1.25 msec (800 power control bits per sec)
A 20ms frame is organized into 16 time intervals of equal durations
These time intervals, each of 1.25 ms are called power control groups (PCGs). Thus a frame has 16 PCGs.

## Slide 17: Power Control in Wireless Cellular Networks Lecture 5 Outline
Performance Measures
Why Power Control?
Closed-Loop and Open-Loop Power Control
Different Power Control Optimization Problems
Distributed Power Control Algorithms
Some Open Problems

## Slide 18: Possible Objective Functions in Power Control Problems….
Aggregate power consumption
Outage ratio
Sum rate (System Throughput)
Fairness
System Throughput and fairness
Notes: Suppose tow transmit power vector and compare them based on above objective functions

## Slide 19: Some Power Control Problems
Minimum aggregate power consumption subject to target-SIR
Minimum outage ratio
where

## Slide 20: Some Power Control Problems
Maximizing aggregate SIR
Maximizing system throughput subject to a minimum target-SIR constraint

## Slide 21: Some Power Control Problems
Max-min SIR (fairness)

## Slide 22: Possible Objective Functions in Power Control Problems…
Suppose tow transmit power vector and compare them based on above objective functions
…..
Notes: Suppose tow transmit power vector and compare them based on above objective functions

## Slide 23: Power Control in Wireless Cellular Networks Lecture 5 Outline
Performance Measures
Why Power Control?
Closed-Loop and Open-Loop Power Control
Different Power Control Optimization Problems
Distributed Power Control Algorithms
  Criteria for Evaluation and Analysis of Distributed Power Control
  Convergence Analysis Framework for Distributed Power Control Algorithms
  Existing Distributed Power Control Algorithms
Some Open Problems

## Slide 24: Distributed Power Control Algorithms
Power updating function
Distributed unconstrained power control algorithm
Distributed constrained power control algorithm

## Slide 25: Distributed Power Control Algorithms
We say that a distributed algorithm converge, if there exist a s.t.,
for we have , i.e.,
Fixed-Point
Fixed-Point Equation:
Where may a distributed power control algorithm converge to? Fixed-Point(s)
, ,…,

## Slide 26: Distributed Power Control Algorithms- Analysis
Fixed-point existence
  Is there exist any fixed-point for power updating function?
  unconstrained case:
  constrained case: { }
Convergence analysis
  Does the distributed power control algorithm converge to its fixed-point?
Objective function
  What objective function is satisfied at the fixed-point (where the algorithm converge to)?
Notes: In step 1 and 2 above, we obtain the fixed points using theoretical framework and in step 3 we investigate that the obtained fixed-point optimizes which objective function.

## Slide 27: Distributed Power Control Algorithms- Analysis
Required information by each user to update its transmit power
Rate of convergence
Sensitivity analysis
  Robust design

## Slide 28: Power Control in Wireless Cellular Networks Lecture 5 Outline
Performance Measures
Why Power Control?
Closed-Loop and Open-Loop Power Control
Different Power Control Optimization Problems
Distributed Power Control Algorithms
  Criteria for Evaluation and Analysis of Distributed Power Control
  Convergence Analysis Framework for Distributed Power Control Algorithms
  Existing Distributed Power Control Algorithms
Some Open Problems

## Slide 29: Distributed Power Control (DPC)
Existing frameworks for fixed-point existence and convergence analysis
  Existing DPC Algorithms (Objective functions, Required information by each user to update its transmit power, Rate of convergence, Sensitivity analysis)

## Slide 30: Existing Theoretical Frameworks for Convergence Analysis of DPC Algorithms
Standard Type I
  R. D. Yates, “A framework for uplink power control in cellular radio systems,” IEEE Journal on Selected Areas in Communications,1995.
Standard Type II
Generalized Framework
  C. W. Sung and K. Leung, “A generalized framework for distributed power control in wireless networks,” IEEE Transactions on Information Theory, 2005.

## Slide 31: Existing Distributed Power Control Algorithms
Existing DPC Algorithms
  Target-SIR tracking power control (TPC)
  Target-SIR tracking power control with permanent removal (TPC-PR)
  Target-SIR tracking power control with temporary removal (TPC-TR)
  Pareto and energy efficient target-SIR tracking with feasibility check (DFC)
  Opportunistic power control (OPC)
  Dynamic target-SIR tracking power control (DTPC)

## Slide 32: Theoretical Frameworks for Convergence Analysis of DPC Algorithms
  To study convergences of distributed power control algorithms, one may use one of three theoretical framework
  Standard Type I (Yates, 1995)
    Type-I monotonicity: if then
    Type-I scalability: for all ,
  Standard Type II (Sung and Leung, 2005)
    Type-II monotonicity: if then
    Type-II scalability: for all ,
  Generalized Framework (Sung and Leung, 2005)
    Two sided scalability: for all , implies
TPC
OPC
TPC-SR, DTPC

## Slide 33: Theoretical Frameworks for Convergence Analysis of DPC Algorithms
  Wide-sense Standard: is said to be wide-sense standard if each of its components, is either standard type I or type II.
  Theorem: A wide-sense standard function is two-sided scalable.
    The following example shows that the converse is not true. The iterative function
    is a two sided scalable function. However it is neither standard type I nor type II, since the monotonicity properties do not hold.

## Slide 34: Theoretical Frameworks for Convergence Analysis of DPC Algorithms
  Given two iterative functions, and , define
    and
    where the minimum or maximum operation is applied component-wise.
    Theorem: if and are two-sided scalable functions, then and are also two-sided scalable functions.

## Slide 35
Van diagram for these three framework
………..

## Slide 36: Theoretical Frameworks for Convergence Analysis of DPC Algorithms
Main theorem:
If a given power-update function is standard type I or standard type II, or two-sided scalable then
  if the power update function has a fixed-point, then it is unique.
  if the power update function has a fixed-point, then the power vector converges to in both synchronous and asynchronous power updating cases

## Slide 37: Theoretical Frameworks for Convergence Analysis of DPC Algorithms
Main theorem:
  Given a two sided scalable function, if there exists such that for all then a fixed point exists

## Slide 38: Power Control in Wireless Cellular Networks Lecture 5 Outline
Performance Measures
Why Power Control?
Closed-Loop and Open-Loop Power Control
Different Power Control Optimization Problems
Distributed Power Control Algorithms
  Criteria for Evaluation and Analysis of Distributed Power Control
  Convergence Analysis Framework for Distributed Power Control Algorithms
  Existing Distributed Power Control Algorithms
Some Open Problems

## Slide 39: Distributed Power Control (DPC)
Existing DPC Algorithms
  Target-SIR tracking power control (TPC)
  Target-SIR tracking power control with permanent removal (TPC-PR)
  Target-SIR tracking power control with temporary removal (TPC-TR)
  Pareto and energy efficient target-SIR tracking with feasibility check (DFC)
  Opportunistic power control (OPC)
  Dynamic target-SIR tracking power control (DTPC)

## Slide 40: Power Control Papers-To be reviewed
Existing theoretical frameworks for convergence analysis
  Standard Type I
    R. D. Yates, “A framework for uplink power control in cellular radio systems,” IEEE Journal on Selected Areas in Communications,1995.
  Generalized Framework
    C. W. Sung and K. Leung, “A generalized framework for distributed power control in wireless networks,” IEEE Transactions on Information Theory, 2005.
Existing distributed power control algorithm
  TPC
    G. J. Foschini, and Z. Milijanic, “A simple distributed autonomous power control algorithm and its convergence,” IEEE Transactions on Vehicular Technology, 1993.
  TPC-PR
    M. Andersin, Z. Rosberg, and J. Zander, “Gradual removals in cellular PCS with constrained power control and noise," ACM/Baltzar Wireless Netw. J., 1996.

## Slide 41: Power Control Papers-To be reviewed
  TPC-TR
    F. Berggren, R. Jantti, and S. Kim, “A generalized algorithm for constrained power control with capability of temporary removal,” IEEE Transactions on Vehicular Technology, 2001.
  TPC-SR
    M. Rasti and A. R. Sharafat, “Distributed power control with soft removal in wireless networks,” IEEE Transactions on Communications, 2011.
  DFC
    M. Rasti, A. R. Sharafat, and J. Zander, “A Distributed Pareto and energy efficient power control algorithm with Feasibility Check in wireless networks”, IEEE Transactions on Information Theory, 2010.

## Slide 42: Power Control Papers-To be reviewed
OPC
  K. Leung and C. W. Sung, “An opportunistic power control algorithm for cellular network,” IEEE/ACM Transaction on Networking, vol. 14, no. 3, pp. 470-478, June 2006.
DTPC
  M. Rasti, A. R. Sharafat, and J. Zander, “A distributed dynamic target-SIR tracking power control algorithm for wireless cellular networks,” IEEE Transactions on Vehicular Technology, Feb. 2010.

## Slide 43: Two Main Distributed Power Control Algorithm
DPC Algorithm | Optimization Problem (Objective Function) | Assumption
Target-SIR Tracking Power Control (TPC) | Minimum aggregate transmit power subject to users’ target-SIR | Each user has a target-SIR System is feasible
Opportunistic Power Control (OPC) | Maximum System throughput | No user has a predefined target-SIR

## Slide 44: Distributed Power Control (DPC)
DPC Algorithm | Optimization Problem (Objective Function) | Assumption
Target-SIR Tracking Power Control (TPC) | Minimum aggregate transmit power subject to users’ target-SIR | Each user has a target-SIR System is feasible
TPC with Permanent Removal (TPC-PR) | Minimum outage ratio (to address gradual removal problem) | Each user has a target-SIR System is infeasible
TPC with Temporary Removal (TPC-TR) |  | 
TPC with soft removal (TPC-SR) |  | 
Pareto and energy efficient target-SIR tracking with feasibility check (DFC) |  | 
Opportunistic Power Control (OPC) | Maximum System throughput | No user has a predefined target-SIR
Dynamic target-SIR tracking power control (DTPC) | Maximum System throughput subject to a minimum target-SIR constraint | Each user has a target-SIR

## Slide 45: Lecture 5 Outline
  Existing Distributed Power Control Algorithms
    TPC,TPC-PR,TPC-TR, TPC-SR, DFC
    OPC, DTPC

## Slide 46: Target-SIR Tracking Power Control (TPC)
Corresponding Optimization Problem:
Minimum aggregate power consumption subject to target-SIR

## Slide 47: Target-SIR Tracking Power Control (TPC)
If interference at time is then at time transmit power should be set to

## Slide 48: Target-SIR Tracking Power Control (TPC)
Unconstrained TPC:
Constrained TPC:
Ri
pi
TPC

## Slide 49: Target-SIR Tracking Power Control (TPC)- Analysis
Q: Check if TPC power update function is a type-I or type-II standard or two-sided scalable function ?
Fixed-point existence
  TPC power update function is a type I standard function
Notes: In step 1 and 2 above, we obtain the fixed points using theoretical framework and in step 3 we investigate that the obtained fixed-point optimizes which objective function.

## Slide 50: Target-SIR Tracking Power Control (TPC)- Analysis
Fixed-point existence
  Unconstrained TPC:
    There exist a unique fixed-point when the system is feasible
    There is no fixed-point for TPC power update function when the system is infeasible.
  Constrained TPC
    There exist a unique fixed-point in both feasible and infeasible systems.
Notes: In step 1 and 2 above, we obtain the fixed points using theoretical framework and in step 3 we investigate that the obtained fixed-point optimizes which objective function.

## Slide 51: Target-SIR Tracking Power Control (TPC)- Analysis
Convergence analysis
  if the TPC power update function has a unique fixed-point, then the power vector converges to in both synchronous and asynchronous power updating cases
  If the system is infeasible, since target-SIRs are rigidly tracked, all users increase their transmit power at each step and thus, the unconstrained TPC diverges
Notes: In step 1 and 2 above, we obtain the fixed points using theoretical framework and in step 3 we investigate that the obtained fixed-point optimizes which objective function.

## Slide 52: Target-SIR Tracking Power Control (TPC)- Analysis
Objective function
  If the system is feasible, TPC solves the following optimization in a distributed manner.
Notes: In step 1 and 2 above, we obtain the fixed points using theoretical framework and in step 3 we investigate that the obtained fixed-point optimizes which objective function.

## Slide 53: Distributed Power Control Algorithms- Analysis
Required information by each user to update its transmit power
Rate of convergence
Sensitivity analysis
  Robust design

## Slide 54: Target-SIR Tracking Power Control (TPC)
If interference at time is then at time transmit power should be set to
=
Notes: Another way of reducing required information is that the total received from all users is broadcasted by base station to users.

## Slide 55: Target-SIR Tracking Power Control (TPC)
TPC Power Updating Function
or equivalently

## Slide 56: Distributed Target-SIR Tracking Power Control (TPC)
Unconstrained TPC:
Constrained-TPC
Ri
pi
TPC
TPC and Closed-Loop-based power control is equivalent

## Slide 57: Numerical Results
TPC in a 5-users system

## Slide 58: Numerical Results: Constrained TPC in feasible System

## Slide 59: Numerical Results: Constrained TPC in Infeasible System

## Slide 60: Numerical Results: Constrained TPC in Infeasible System
TPC

## Slide 61: Drawbacks of TPC
If the target-SIRs are not attainable, the conventional TPC or closed-loop based power control algorithms results in an maximum transmission by all non-supported users
  inefficient power consumption
  increased number of non-supported users
A Straightforward Solution
  All non-supported users are removed (too many unnecessary removals!), which is currently implemented in existing (closed-loop based) standards
Gradual Removal Problem

## Slide 62: Drawbacks of TPC
Gradual Removal Problem
  Designing a (centralized or distributed) mechanism to check the feasibility
  When the system is infeasible, least number of users should be temporarily removed
Gradual removal problem is a NP-hard problem
There exits no power control scheme (whether distributed or centralized) with capabilities of gradual removal and feasibility check

## Slide 63: The Problem Statement
Gradual Removal Algorithm
  Designing a distributed mechanism to check the feasibility
  When the system is infeasible, least number of users should be temporarily removed

## Slide 64: Gradual Removal Problem: Motivating Example
Consider 4 users whose path-gains are given by
and noise plus inter-cell interference is . By running the TPC or equivalently the closed-loop power control, for the target-SIR vector of , the following results are obtained.
Received SIR/Tranmit Power |  | 
 | 1 | 0
 | 1 | 0.75
 | 1 | 0.70
 | 0.73 | 0.50
Users 1 to 3 transmit at their maximum power without reaching their target-SIR
If users 1 is removed, then the remaining users reach their target-SIR consuming less power

## Slide 65: Existing Gradual Removal Algorithms
DPC Algorithm | Optimization Problem (Objective Function) | Assumption
Target-SIR Tracking Power Control (TPC) | Minimum aggregate transmit power subject to users’ target-SIR | Each user has a target-SIR System is feasible
TPC with Permanent Removal (TPC-PR) | Minimum outage ratio (to address gradual removal problem) | Each user has a target-SIR System is infeasible
TPC with Temporary Removal (TPC-TR) |  | 
TPC with soft removal (TPC-SR) |  | 
Pareto and energy efficient target-SIR tracking with feasibility check (DFC) |  | 

## Slide 66: Lecture 5 Outline
  Existing Distributed Power Control Algorithms
    TPC,TPC-PR,TPC-TR, TPC-SR, DFC
    OPC, DTPC